SCUBA-2 Block Specification

addr_card

Created on:   	4 October 2005

Last saved on:	06 October 2005

Table of Contents

1.	Block Description	3

1.1	Block Hierarchy	3

1.2	Block Overview and Features	3

1.3	Detailed Description	3

2.	Interface Description	5

2.1	Signals Description	5

Files Associated with this Block	7

# Block Description

The addr_card is the top-level block in the hierarchy of the RTL-level code for the Address-card FPGA.

## Block Hierarchy

Figure 1: addr_card Block Location Within the System

## Block Overview and Features

The addr_card top level communicates to the external devices including the 41 parallel DACs, LEDs, id/thermo chip, and EEPROM.

## Detailed Description

The Wishbone bus protocol (refer to Wishbone Specification) is adopted as inter-block communication standard between the different blocks in addr_card. One block, in this case dispatch, acts as Wishbone Master and the other blocks are Wishbone slaves. Commands are received along the backplane LVDS line and then decoded by the Wishbone Master and communicated to the relevant Wishbone Slave through the Wishbone protocol.

The following blocks are instantiated in addr_card block:

- ac_dac_ctrl:

  - This block controls all the parallel DACs.

- frame_timing:

  - This block controls the overall timing and ensures the coherence of the operations of the different blocks.

- dispatch:

  - Receives and decodes the incoming backplane commands

  - Delivers the wishbone-formatted command to the appropriate wishbone slave

  - Converts the wishbone reply to backplane format and transmits the reply over the backplane.

- id/thermo: A wishbone slave to read the card-id and the temperature from the DS8020 chip

- leds:  A wishbone slave to controls the 3 LEDs

- fw_rev: A wishbone slave to return the firmware revision

For more information, refer to the documentation for each block.

Figure 2: addr_card Block Diagram

# Interface Description

## Signals Description

|  | Description | Direction |
| --- | --- | --- |
| Global Signals |
| rst_n | Global reset signal | In |
| Inclk | PLL input clock | in |
| Interface to Parallel DACs |
| dac_ data0 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data1 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data2 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data3 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data4 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data5 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data6 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data7 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data8 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data9 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_ data10 | 14-bit data for the parallel DAC shared between 4 DACs | out |
| dac_clk | 41-bit clock for DAC0 to DAC40 with each bit being the clock for one of the DACs | out |
| LVDS Interface |
| lvds_cmd | receives incoming commands over the backplane LVDS line. The backplane signal is a multi-drop signal that originates from clock card and goes to all the cards. | in |
| lvds_sync | incoming sync signal over the backplane LVDS line | in |
| lvds_spare | connected to a spare backplane LVDS line for future use | in |
| lvds_txa | used to transmit the reply to a command over a backplane LVDS line. The backplane line is a dedicated line between readout card and clock card. | out |
| lvds_txb | connected to a spare backplane LVDS line for future use. The backplane line is a dedicated line between readout card and clock card. | out |
| EEPROM Interface |
| eeprom_si | Incoming serial data from eeprom as part of the SPI interface | in |
| eeprom_so | Outgoing serial data to eeprom as part of the SPI interface | out |
| eeprom_sck | Serial clock for eeprom (SPI interface) | out |
| eeprom_cs | Chip select for eeprom (SPI interface) | out |
| TTL Interface (X 3 for TTL1 to TTL3 spare lines) *Note: Clock card uses ttl1 line to send down the global firmware reset to all the cards |
| ttl_txena1 | controls the direction of the spare TTL line | out |
| ttl_nrx1 | input TTL spare line controlled by ttl_txena1 | in |
| ttl_tx1 | output TTL spare line controlled by ttl_txena1 | out |
| LED Interface |
| red_led | Red LED data | out |
| ylw_led | Yellow LED data | out |
| grn_led | Green LED data | out |
| Miscellaneous |
| dip_sw3 | dip switch 3 data | in |
| dip_sw4 | dip switch 4 data | in |
| wdog | watchdog | out |
| slot_id | 4-bit data hard-wired per slot on the backplane | in |
| card_id | single-wire interface to the on-board ds8020 id/temperature chip | in |
| test | 32-bit PTH test header | out |
| mictor | 32-bit data for the logic analyzer | out |
| mictorclk | 2-bit mictor clock pins for the logic analyzer | out |
| rs232_rx | Debug port | in |
| rs232_tx | Debug port | out |

# Files Associated with this Block

| File | Description |
| --- | --- |
| addr_card.vhd | top-level |
| addr_card_pack.vhd | pack file for addr_card.vhd including definition of some of the constants |
| packet.hex | used to emulate backplane-format commands in conjunction with tb_addr_card_self_test.vhd |
| tb_addr_ card_self_test.vhd | testbench for addr_card top-level using packet_hex to emulate backplane commands |
| tb_addr_card.vhd | Testbench for addr_card top-level using a clok_card instantiation to emulate backplane commands. |

# Text boxes

addr_card

dispatch

ac_dac_ctrl_wbs

frame_timing

id_thermo

fw_rev

leds

ac_dac_ctrl_core

ac_dac_ctrl