SCUBA-2 Block Specification

LVDS Transmitter

November 14, 2004

Table of Contents

1.	Block Overview	3

1.1	Block Location and Block Interface Within System	3

1.2	Block Functionality / Features	3

1.3	Block Dataflow	3

2.	Block Interfaces	4

2.1	Interface Signal Description	4

2.2	Interface Protocol and Timing	5

3.	High-Level Description	8

3.1	State Machine Description	8

3.2	Special Optimizations	8

4.	Files of the Block	9

4.1	Source Code	9

4.1.1	lvds_tx.vhd	9

4.2	Header Code	9

5.	Naming Conventions Used	10

# Block Overview

## Block Location and Block Interface Within System

The LVDS transmitter is used by the following modules:

- cmd_queue

- dispatch

## Block Functionality / Features

- Accepts a 32-bit word and transmits it over an LVDS serial link (four transmit cycles of 8-bits each)

- Indicates transmission status using a busy signal.

## Block Dataflow

# Block Interfaces

## Interface Signal Description

Interface Signals

| Signal | Description | Direction |
| --- | --- | --- |
| Global Signals |
| clk_i | Global clock signal | in |
| comm_clk_i | Global communications clock signal | in |
| rst_i | Global asynchronous active-high reset | in |
| Data and Status Signals |
| dat_i | Parallel input data (32-bit word) to be sent. | in |
| rdy_i | Ready signal. Indicates that the data on dat_i is valid. | in |
| busy_o | Busy signal. Indicates that the module is transmitting. | out |
| LVDS Output |
| lvds_o | Serial output data to LVDS drivers. The output stream is framed according to RS-232 protocol. | out |

## Interface Protocol and Timing

# High-Level Description

## State Machine Description

Transmit controller state diagram:

Transmit controller state outputs:

| Present State | Output Signal |
| --- | --- |
|  | tx_rdy | buffer_ena | byte_count_ena | byte_count_clr | busy_o | tx_data |
| IDLE | 0 | 1 | 1 | 1 | 0 | “00000000” |
| TX | 1 | 0 | 0 | 0 | 1 | byte from buffer |
| TXBUSY | 0 | 0 | 0 | 0 | 1 | “00000000” |
| SETUP | 0 | 0 | 1 | 0 | 1 | “00000000” |
| DONE | 0 | 0 | 0 | 0 | 1 | “00000000” |

# Files of the Block

## Source Code

### lvds_tx.vhd

This file contains the LVDS transmitter implementation.  It is compiled into the “work” library.

## Header Code

Not applicable for this block

# Naming Conventions Used

# Text boxes

clk_i

rst_i

Transmit Controller

Byte Counter

async_tx

Data Buffer

Clock Divider

dat_i

rdy_i

busy_o

comm_clk_i

lvds_o

lvds_tx

idle

tx

tx busy

setup

done

rdy_i = ‘1’

tx_busy = ‘1’

tx_busy = ‘0’

tx_busy

tx_busy = ‘1’

tx_busy = ‘0’

byte_count < 3

byte_count = 3

rdy_i = ‘0’

byte_count

tx_data

buffer_out

tx_rdy