SCUBA-2 Block Specification

fsfb_ctrl

Revision History:

Rev. 1.0 MN Initial Release

Rev. 1.1 MA added document number and revision history

September 15, 2006

Table of Contents

1.	Block Overview	3

1.1	Block Location and Block Interface within System	3

1.2	Block Functionality / Features	3

1.3	Block Dataflow	4

2.	Block Interfaces	5

2.1	Interface Signal Description	5

2.2	Interface Protocol and Timing	5

3.	High-Level Description	7

3.1	State Machine Descriptions	7

3.2	Special Optimizations	8

4.	Files of the Block	9

4.1	Source Code	9

4.1.1	Source1.vhd	9

4.2	Header Code	9

4.2.1	Header1.vhd	9

5.	Naming Conventions Used	10

# Block Overview

## Block Location and Block Interface within System

The fsfb_ctrl is a component in flux_loop_ctrl.  The flux_loop_ctrl is instantiated eight times, one per channel, in the flux_loop block of a Readout Card.

As illustrated in Figure 1, the fsfb_ctrl interfaces with the following blocks:

- The DAC of the Readout card;

- The frame_timing block on the Readout card;

- The fsfb_calc in the flux_loop_ctrl.

Figure 1: Location of fsfb_ctrl in the System.

## Block Functionality / Features

The fsfb_ctrl block receives the 32-bit data, fsfb_ctrl_dat_i(31..0), to be applied to DAC.  Since DAC input data is only 14 bits, fsfb_ctrl selects only 14 bits from the input data, e.g., fsfb_ctrl_dat_i(25..12).  The selection is based on a generic value that has a default value of (13..0).  If not in lock mode, fsfb_ctrl sends the data as is to the DAC and issues a DAC clock enable signal under the control of dac_dat_en_i from the frame_timing block.  However, if it is in lock mode indicated by the fsfb_calc block, fsfb_ctrl runs the input data through a conversion map.  The conversion map is to convert the input 2’s complement to a binary output.  This conversion map needs to know the polarity of conversion in the ADC.  This latter information is provided to fsfb_ctrl using a generic value.  Finally, the converted data is sent to the DAC and a DAC clock is asserted under the control of the dac_dat_en_i from the frame_timing block.

## Block Dataflow

Figure 2 represents the dataflow for fsfb_ctrl.

Figure 2: The fsfb_ctrl block dataflow.

# Block Interfaces

## Interface Signal Description

Interface Signals

| Signal | Description | Direction |
| --- | --- | --- |
| Global Signals |
| rst_i | Global reset | in |
| clk_50_i | Global clock | in |
| Frame_timing Interface |
| dac_dat_en_i | Indicates the window to send data to the DAC | in |
| fsfb_calc Interface |
| fsfb_ctrl_dat_i | Input data from upstream block | in |
| fsfb_ctrl_dat_rdy_i | Asserted for one clock cycle when the data input is valid | in |
| fsfb_ctrl_lock_en_i | When high, it indicates that the flux_loop_ctrl is in lock mode | in |
| DAC Interface |
| dac_dat_o | Data to the DAC | out |
| dac_clk_o | Enable clock to DAC | out |

## Interface Protocol and Timing

Figure 3 illustrates the interface protocol timing.

Figure 3: Timing for Interface Signals.

As shown in Figure 3, dac_dat_en_i can change at any time with respect to fsfb_ctrl_dat_rdy_i.  Therefore, dac_clock_o is asserted if both fsfb_ctrl_dat_rdy_i and dac_dat_en_i have been asserted.

# High-Level Description

## State Machine Descriptions

The Algorithmic State Machine (ASM) for the fsfb_ctrl is shown in Figure 4.

Figure 4: The fsfb_ctrl Algorithmic State Machine.

A timing diagram representation of the control signals for the fsfb_ctrl is shown in Figure 5.

Figure 5: The fsfb_ctrl Control Signals Timing.

## Conversion Map

As seen in Figure 2, the data from fsfb_calc is passed through a conversion map.  The values from fsfb_calc are either negative or positive and range between –n to +n.  However DAC is unipolar, and, hence, DAC value need to vary between 0 to N.  Moreover, a positive change in the circuitry connected to the ADC can result in a negative or positive value at the output of the ADC.  The DAC output needs to compensate for the change at the input of the ADC.  Therefore, the following scenarios are possible:

Straight Polarity

In this case, a positive change in the circuitry connected to the ADC input results in a positive ADC value.  Therefore, (-n..+n) from fsfb_calc needs to map to (0..N) in DAC.  To achieve this, one could add |n| to the fsfb_calc value.  However, a closer analysis reveals that a simple inversion of fsfb_calc most significant bit will result in the correct conversion.

Reverse Polarity

In this case, a positive change in the circuitry connected to the ADC input results in a negative ADC value, and vice versa.  Therefore, (-n..+n) from fsfb_calc needs to map to (N..0) in DAC.  To achieve this, one could subtract |n-1| from the fsfb_calc value and then convert the sign.  As an example, an input value of -6 (4-bit representation) would map to |-6-7|=13.  As another example, an input value of 2 would map to –(2-7)=5.  However, a closer analysis reveals that a simple inversion of the all the fsfb_calc bits except for the most significant bit will result in the correct conversion.

## Special Optimizations

# Files of the Block

## Source Code

### Source1.vhd

## Header Code

### Header1.vhd

# Naming Conventions Used

# Text boxes

DAC

fsfb_calc

frame_timing

fsfb_ctrl

flux_loop_ctrl

To DAC

F

F

fsfb_ctrl_lock_en_i

From fsfb_calc

enb

fsfb_ctrl_dat_rdy_i

Conversion Map

F

F