SCUBA-2 Block Specification

readout_card

Revision History:

Rev. 1.0 MA Initial Release

Rev. 1.1 MA added document number and revision history

Created on:   	4 October 2005

Last saved on:	15 September 2006

Table of Contents

1.	Block Description	3

1.1	Block Hierarchy	3

1.2	Block Overview and Features	3

1.3	Detailed Description	3

2.	Interface Description	5

2.1	Signals Description	5

Files Associated with this Block	7

# Block Description

This is the top-level block in the hierarchy of the RTL-level code for the readout-card FPGA.

## Block Hierarchy

Figure 1

## Block Overview and Features

The readout card top level communicates to the external devices including the data sampling ADC, the parallel DAC to control S1_FB, and the SPI DACs to control the offset and bias of the series array (sa_bias and sa_offset).

## Detailed Description

The Wishbone bus protocol (refer to Wishbone Specification) is adopted as inter-block communication standard between the different blocks in readout_card. One block, in this case dispatch, acts as Wishbone Master and the other blocks are Wishbone slaves. Commands are received along the backplane LVDS lines and then decoded by the Wishbone Master and communicated to the relevant Wishbone Slave through the Wishbone protocol.

The following blocks are instantiated in readout_card block:

- flux_loop :

  - Instantiates 8 separate instances of the flux_loop_ctrl block, one for each channel. The flux_loop_ctrl controls the ADC and determines the data that has to be applied to the S1_FB DAC depending on the mode of operation.  There are three modes of operations: lock mode (with PIC controller), ramp mode and constant mode. Depending on the data mode settings, the appropriate data is delivered on the wishbone bus.

  - Handles all the flux_loop-related wishbone commands

  - Instantiates an fsfb_corr block to handle flux-jumping for all 8 channels in lock mode

- frame_timing:

  - This block controls the overall timing and ensures the coherence of the operations of the different blocks.

- dispatch:

  - Receives and decodes the incoming backplane commands

  - Delivers the wishbone-formatted command to the appropriate wishbone slave

  - Converts the wishbone reply to backplane format and transmits the reply over the backplane.

- id/thermo: A wishbone slave to read the card-id and the temperature from the DS8020 chip

- leds:  A wishbone slave to controls the 3 LEDs

- fw_rev: A wishbone slave to return the firmware revision

For more information, refer to the documentation for each block.

Figure 2: Readout_card Block Diagram

The following block diagram shows the more detailed view of the flux_loop_ctrl block instantiated for each channel:

# Interface Description

## Signals Description

|  | Description | Direction |
| --- | --- | --- |
| Global Signals |
| rst_n | Global reset signal | In |
| inclk | PLL input clock | in |
| ADC Interface (X 8 for ADC1 to ADC8) |
| adc1_dat | ADC1 14-bit digital data | in |
| adc1_ovr | ADC1 over-range bit | in |
| adc1_rdy | ADC1 data ready signal | in |
| adc1_clk | ADC1 Encode signal, conversion initiated on rising edge | out |
| Feedback DAC Interface (X 8 for DAC1 to DAC8) |
| dac_FB1_dat | Feedback DAC1 14-bit data | out |
| dac_FB_clk | Feedback DAC clock (common to DAC1 to DAC8) | out |
| Offset and SA_Bias DAC Interface |
| dac_ dat | 8-bit data for DAC1 to DAC8, each bit is the serial data for the SPI DAC and is shared between the sa_bias and offset DACs. | out |
| dac_clk | 8-bit-wide clock for DAC1 to DAC8, each bit is the clock for the SPI DAC and is shared between the sa_bias and offset DACs | out |
| bias_dac_ncs | 8-bit wide chip select for DAC1 to DAC8, each bit is the chip select for the sa_bias SPI DAC | out |
| offset_dac_ncs | 8-bit wide chip select for DAC1 to DAC8, each bit is the chip select for the offset SPI DAC | out |
| LVDS Interface |
| lvds_cmd | receives incoming commands over the backplane LVDS line. The backplane signal is a multi-drop signal that originates from clock card and goes to all the cards. | in |
| lvds_sync | incoming sync signal over the backplane LVDS line | in |
| lvds_spare | connected to a spare backplane LVDS line for future use | in |
| lvds_txa | used to transmit the reply to a command over a backplane LVDS line. The backplane line is a dedicated line between readout card and clock card. | out |
| lvds_txb | connected to a spare backplane LVDS line for future use. The backplane line is a dedicated line between readout card and clock card. | out |
| TTL Interface (X 3 for TTL1 to TTL3 spare lines) *Note: Clock card uses ttl1 line to send down the global firmware reset to all the cards |
| ttl_dir1 | controls the direction of the spare TTL line | out |
| ttl_in1 | input TTL spare line controlled by ttl_dir1 | in |
| ttl_out1 | output TTL spare line controlled by ttl_cdir1 | out |
| LED Interface |
| red_led | Red LED data | out |
| ylw_led | Yellow LED data | out |
| grn_led | Green LED data | out |
| Miscellaneous |
| dip_sw3 | dip switch 3 data | in |
| dip_sw4 | dip switch 4 data | in |
| wdog | watchdog | out |
| slot_id | 4-bit data hard-wired per slot on the backplane | in |
| card_id | single-wire interface to the on-board ds8020 id/temperature chip | in |
| mictor | 32-bit data for the logic analyzer | out |

# Files Associated with this Block

| File | Description |
| --- | --- |
| readout_card.vhd | top-level |
| readout_card_pack.vhd | pack file for readout_card.vhd including definition of some of the constants |
| packet.hex | used to emulate backplane-format commands in conjunction with tb1_readout_card.vhd and clk_card.vhd |
| tb1_readout_card.vhd | testbench for readout_card top-level |
| clk_card.vhd | top-level clock card instantiated in tb_readout_card.vhd in order to issue the backplane formatted commands. In CVS, refer to the branch called: rc_v1_firmware_validation. |

# Text boxes

id_thermo

fw_rev

leds

readout_card

dispatch

fsfb_corr

frame_timing

wbs_fb_data

wbs_frame_data

flux_loop_ctrl ch8

flux_loop_ctrl ch7

flux_loop_ctrl ch6

flux_loop_ctrl ch5

flux_loop_ctrl ch4

flux_loop_ctrl ch3

flux_loop_ctrl ch2

fsfb_corr

SPI

DAC

SPI

DAC

offset_ctrl

sa-bias_ctrl

adc_sample_coadd

io_ctrl

fsfb_calc

filter_regs

filtter_Q

fsfb_Q_bank0

fsfb_Q_bank1

fsfb_proc

ramp

const

pidz

+

filter

fsfb_ctrl

flux_loop_ctrl

wbs_fb_data

wbs_frame_data

ADC

frame_timing

DAC

Figure 3: Flux_loop_ctrl Block Diagram

flux_loop_ctrl ch1

flux_loop