SCUBA-2 Block Specification

wbs_fb_data

Revision History:

Rev. 1.0 MN Initial Release

Rev. 1.1 MA added document number and revision history

September 15, 2006

Table of Contents

1.	Block Overview	3

1.1	Block Location and Block Interface within System	3

1.2	Block Functionality / Features	3

1.3	Block Dataflow	4

1.3.1	Top Level Dataflow	4

1.3.2	The p_banks_admin Dataflow	5

1.3.3	The misc_banks_admin Dataflow	5

2.	Block Interfaces	7

2.1	Interface Signal Description	7

2.2	Interface Protocol and Timing	9

3.	High-Level Description	10

3.1	Timing Description	10

3.2	Special Optimizations	12

4.	Files of the Block	13

4.1	Source Code	13

4.1.1	Source1.vhd	13

4.2	Header Code	13

4.2.1	Header1.vhd	13

5.	Naming Conventions Used	14

# Block Overview

## Block Location and Block Interface within System

The wbs_fb_data is located on the Readout card FPGA.  It is a wishbone slave and it interfaces with the following blocks:

- Dispatch (wishbone master);

- The flux_loop_ctrl (8 instances).

Figure 1: Location of wbs_fb_data in the Readout card FPGA.

## Block Functionality / Features

The wbs_fb_data is a wishbone slave and has to be able to process wishbone read and write instructions.  Moreover, it provides data to flux_loop_ctrl blocks.  The wbs_fb_data receives data for the following parameters from the dispatch and provides them to the downstream block: P/I/D/Z, adc_offset, filter_coeff, servo_mode, ramp_step_size, ramp_amp, const_val, num_ramp_frame_cycles, sa_bias, and offset_dat.  The wbs_fb_data will also provide the data stored for these parameters to the dispatch upon the dispatch read request.

Data for P/I/D/Z, and adc_offset are stored in RAM blocks.  However, the data for the rest of the parameters are stored in registers.

## Block Dataflow

To manage the complexity, wbs_fb_data uses five identical memory bank administrator (p-banks_admin, i_banks_admin, d_banks_admin, z_bank_admin, and adc_sample_banks_admin) and one miscellaneous memory bank administrator for the remaining parameters.

### Top Level Dataflow

Figure 2 represents a top level view of the dataflow in wbs_fb_data.

Figure 2: The wbs_fb_data block dataflow.

### The p_banks_admin Dataflow

Figure 3 illustrates the dataflow in the p_banks_admin block.  As mentioned earlier, the memory bank administrators for I/D/Z and adc_sample parameters are identical to the p_banks_admin block.

Figure 3: The p-banks_admin dataflow.

### The misc_banks_admin Dataflow

The misc_banks_admin block instantiates several registers for the following parameters:

- filter_coeff (seven values in total);

- servo_mode;

- ramp_step_size;

- ramp_amp;

- const_val;

- num_ramp_frame_cycles;

- sa_bias_dat  (one for each channel);

- offset_dat (one for each channel).

The dataflow of misc_banks_admin is illustrated in Figure 4 where the block numbers correspond to the following indices:

- Block number 0-6 for filter_coeff

- Block number 7 for servo_mode;

- Block number 8 for ramp_step_size;

- Block number 9 for ramp_amp;

- Block number 10 for const_val;

- Block number 11 for num_ramp_frame_cycles;

- Block number 12-19 for sa_bias_dat;

- Block number 20-27 for offset_dat.

Figure 4: The misc_banks_admin dataflow.

# Block Interfaces

## Interface Signal Description

Interface Signals

| Signal | Description | Direction |
| --- | --- | --- |
| Global Signals |
| clk_50_i | Global clock | in |
| rst_i | Global reset | in |
| Per flux_loop_ctrl channel (# must be replaced by 0 to 7) |
| adc_offset_dat_ch#_o | adc_offset data for flux_loop_ctrl channel 0-7. | out |
| adc_offset_addr_ch#_i | Read address from flux_loop_ctrl channel 0-7. | in |
| p_dat_ch#_o | P data for flux_loop_ctrl channel 0-7. | out |
| p_addr_ch#_i | Read address from flux_loop_ctrl channel 0-7. | in |
| i_dat_ch#_o | I data for flux_loop_ctrl channel 0-7. | out |
| i_addr_ch#_i | Read address from flux_loop_ctrl channel 0-7. | in |
| d_dat_ch#_o | D data for flux_loop_ctrl channel 0-7. | out |
| d_addr_ch#_i | Read address from flux_loop_ctrl channel 0-7. | in |
| z_dat_ch3_o | Z data for flux_loop_ctrl channel 0-7. | out |
| z_addr_ch#_i | Read address from flux_loop_ctrl channel 0-7. | in |
| sa_bias_ch#_o | sa_bias data for flux_loop_ctrl channel 0-7. | out |
| offset_dat_ch#_o | offset data for flux_loop_ctrl channel 0-7. | out |
| All flux_loop_ctrl channels |
| filter_coeff0_o | First filter coefficient to all flux_loop_ctrl. | out |
| filter_coeff1_o | Second filter coefficient to all flux_loop_ctrl. | out |
| filter_coeff2_o | Third filter coefficient to all flux_loop_ctrl. | out |
| filter_coeff3_o | Fourth filter coefficient to all flux_loop_ctrl. | out |
| filter_coeff4_o | Fifth filter coefficient to all flux_loop_ctrl. | out |
| filter_coeff5_o | Sixth filter coefficient to all flux_loop_ctrl. | out |
| filter_coeff6_o | Seventh filter coefficient to all flux_loop_ctrl. | out |
| servo_mode_o | servo_mode data for flux_loop_ctrl. | out |
| ramp_step_size_o | ramp_step_size data for flux_loop_ctrl. | out |
| ramp_amp_o | ramp_ampl data for flux_loop_ctrl. | out |
| const_val_o | const_val data for flux_loop_ctrl. | out |
| num_ramp_frame_cycles_o | num_ramp_frame_cycles data for flux_loop_ctrl. | out |
| Dispatch Interface |
| dat_i | Data in from Dispatch | in |
| addr_i | Address from Dispatch showing the address of memory banks. The addr_i is kept constant during a read or write cycle. | in |
| tga_i | Address Tag from Dispatch. The tga_i is incremented during a read or write cycle. Therefore, it is used as an index to the location in the memory bank. | in |
| we_i | Write Enable input from Dispatch. | in |
| stb_i | Strobe signal from Dispatch. Indicates if an address is valid or not. See Wishbone manual page 54 and 57. | in |
| cyc_i | Input from Dispatch indicating a read or write cycle is in progress. | in |
| dat_o | Data out to Dispatch. | out |
| ack_o | Acknowledge signal to Dispatch on completion of any read or write cycle. | out |

## Interface Protocol and Timing

The interface protocol with the Dispatch follows that of the Wishbone protocol.  In addition, the flux_loop_ctrl blocks can read their data independently from the memory banks in the p/i/d/z/adc_sample_banks_admin.  The read cycle for P/I/D/Z and adc_offset parameters is illustrated in Figure 5 for the P parameter as an example.  Moreover, the data in the registers of the misc_banks_admin is available to the flux_loop_ctrl blocks as dedicated inputs.  Note that the system user is responsible to make sure valid data is present in the wbs_fb_data before the flux_loop_ctrl blocks are reading them.

Figure 5: The flux_loop_ctrl read cycle for P/I/D/Z and adc_offset parameter.

# High-Level Description

## Timing Description

The memory banks administrators work in either of three states: Idle, Wishbone_Read, and Wishbone_Write.

For p_banks_admin, Figure 6 illustrates a write cycle. The same timing also applies to I/D/Z and adc_offset banks administrators, and their operation is identical to that of the p_banks_admin.  In Figure 6, following an edge in wren_i, stb_i, and addr_i, data is written into the RAMs where tga_i indicates the location of the memory where the data is stored.  An acknowledge signal is hence generated when the data is written into the memory.  If the wishbone master asserts a wait by lowering stb_i, the block goes into an idle mode.

Figure 6: Write cycle for p_banks_admin.

Figure 7 illustrates a read cycle for p_banks_admin.  The same timing also applies to I/D/Z and adc_offset banks administrators, and their operation is identical to that of the p_banks_admin.  In Figure 7, after two clock cyckes from an edge in wren_i, stb_i, and addr_i, data is read from the RAMs and placed on the dat_o.  Two clock cycles delays are needed as the RAM is registered both at the inputs and the outputs.  In this read process, tga_i indicates the location of the memory where the data is retrieved.  An acknowledge signal is hence generated when the data is read from the memory.  If the wishbone master asserts a wait by lowering stb_i, the block goes into an idle mode.

Figure 7: Read cycle for p_banks_admin.

For misc_banks_admin, Figure 8 illustrates a write cycle. This write cycles is shown for parameter sa_bias as an example of a block write.  However, it applied to other parameters used in misc_banks_admin.  Since a register is used for these parameters, a write cycle is complete in one clock cycle.  Therefore, based on the recommendation of the Wishbone manual, the acknowledge signal is the logical AND of stb_i and cyc_i.  As seen in Figure 8, appropriate wren signals for each register is generated based on the value of tga_i.

Figure 8: Write cycle for misc_banks_admin.

A read cycle for sa_bias parameter in misc_banks_admin is illustrated in Figure 9.  Similarly to the write cycle for misc_banks_admin, the sa_bias read cycle also applies to the read cycle for other parameters in the misc_banks_admin.  Since a register is used for these parameters, a read cycle is complete in one clock cycle.  Therefore, based on the recommendation of the Wishbone manual, the acknowledge signal is the logical AND of stb_i and cyc_i.

Figure 9: Read cycle for misc_banks_admin.

## Special Optimizations

# Files of the Block

## Source Code

### Source1.vhd

## Header Code

### Header1.vhd

# Naming Conventions Used

# Text boxes

flux_loop_ctrl

flux_loop_ctrl

flux_loop_ctrl

To All

flux_loop_ctrl

To

Parent Block

tga_i

addr_i

From Dispatch

wbs_fb_data

flux_loop_ctrl

tga_i

27

To

Respective

flux_loop_ctrl

block

..

To All

flux_loop_ctrl

20

To Dispatch

19

wbs_fb_storage

ch0

addr_i

From Dispatch

..

12

11

0

To

Respective

flux_loop_ctrl

block

To

Parent Block

addr_i

wbs_fb_storage

ch1

wbs_fb_storage

ch7

wbs_fb_storage

ch6

flux_loop_ctrl

wbs_fb_storage

ch5

flux_loop_ctrl

wbs_fb_storage

ch4

wbs_fb_storage

ch3

adc_sample_banks_admin

misc_banks_admin

i_banks_admin

z_banks_admin

d_banks_admin

p_banks_admin

dispatch

flux_loop_ctrl

flux_loop_ctrl

10

9

8

7

wbs_fb_storage

ch2

6

From Dispatch

..

To

flux_loop_ctrl blocks